## Slide 1
LED digital display top mounted
Electronic mixer
Mixing series OS-T40/T60
OS20/OS40/
OS70/OS10 series

## Slide 2
LED LCD display
Monitor actual rotational speed
Wide speed range,50-2200rpm
Pownl

## Slide 3
Strong mixing effect
High output torque
High stirring viscosity,stable
operation,splash proof sample, wide sample range,anti slip pad, stable container

## Slide 5
DC brushless motor explosion-proof/maint enance free
DC brushless motor hasa long service life,explosion-proof,and maintenance free
LED LCD display
Monitoring actual speed hasa
wide range of speeds,50-2200rpm

## Slide 6
Configure constant speed function
Even under conditions of viscosity
changes,the digital feedback control system can ensure constant speed and torque of the agitator
Strong mixing
effect,high output
torque
High stirring viscosity,stable
operation,splash proof sample, wide sample range,anti slip pad, stable container
Silicone protective sleeve
self-locking hand tight drill
chuck
B 脂wentsohen evaporation and corrosion
Overload protection circuit | protection/motor automatic cut-off
Automatically cut off the
circuit and gbund an alarm
in case of abnormal speed or
ofdrill

## Slide 7
A panoramic view of the top-mounted mixer Select the model according to the demand |  |  |  |  |  |  | 
picture | Model Instrument | Maximum mixing volume (water)) | Constant speed function | OSD | range of speed | maximum torque | peak viscosity
 | OS-T40-Plus* | 30L | √ | LCD | 50-2200rpm | 40N ·cm | 10000mPa ·s
 | OS-T60-Plus* | 50L | √ | LCD | 50-2200rpm | 60N ·cm | 50000mPa ·s
 | OS20-Pro | 20L | √ | LCD | 50-2200rpm | 40N ·cm | 10000mPa ·s
 | OS20-S | 20L |  | LED | 50-2200rpm | 40N ·cm | 10000mPa ·s
 | OS40-Pro | 40L | √ | LCD | 50-2200rpm | 60N ·cm | 50000mPa ·s
 | OS40-S | 40L |  | LED | 50-2200rpm | 60N ·cm | 50000mPa ·s
 | OS70-Pro | 70L | 有 | LCD | 50-1100rpm | 300N ·cm | 100000mPa ·s

## Slide 8
OS20-S/OS40-S
LED digital top mounted electronic mixer
Characteristics and
advantages
·Reliable performance and outstanding performance;
·Wide speed range,50-2200rpm;
·DC brushless motor has a long service life,is explosion-proof,and maintenance free; LED LCD display,monitoring actual rotational speed;
.Safety circuit design,automatically cutting off the circuit in case of abnormal speed or overload.
区 中 Top mounted mixing blade set Article number 18900743
It includes a vertical pole,6
mixing blade types:four blade, fan blade,centrifugal,straight, radial,anchor blade,and
disassembly tool.

## Slide 9
Technical Parameter | OS20-S | OS40-S
Maximum mixing volume [water] | 20L | 40L
speed range | 50-2200rpm | 50-2200rpm
MAXIMUM TORQUE | 40Ncm | 60Ncm
Maximum viscosity | 10000mPa.s | 50000mPa.s
Motor type | brushless dc motor | brushless dc motor
Speed display | LED | LED
Overload protection dis play | LED | LED
Dril chuck clamping diameter range | 0.5~10mm | 0.5-10mm
degrees of protoction provided bye nclosure | P21 | IP21
voltage | 100-240V,50/60 Hz | 100-240V,50/60 Hz
Motor input and output power | 60W/50W | 120W/100W
power | 70W | 130W
Size [length xwidth x height] | 83×220x186mm | 83x220×186mm
weight | 2.8kg | 2.8kg
Allow ambient tomperature and humi | dity 5-40℃,80%RH | 5-40℃,80%RH
Universal tablet holder(OS20,40,
70 universal)
Article number 18900605
Size [lengthx widthx height]:
200×315×780mm
Material:Cast Iron
Large flat bracket (OS70 specific)
Article number 18900497
HCH Size [length x width x height]: 335x463×780mm Material:Cast Iron
Flat bracket

## Slide 10
The top mounted design of
the mixing paddle facilitates
container replacement
OS20-Pro/OS40-Pro/ OS70-Pro
LCD CNC top mounted electronic mixer
Start and run smoothly, prevent sample splashing or overflow
Constant speed, can automatically adjust torque according to changes in sample viscosity,
Maintain the set speed
DC brushless motor, long lifespan, maintenance free
Silicone protactive cover prevents solvent evaporati on and corrosion of drill
chuck,avoiding rust
Equipped with safety features such as splash and overload protection
LCD displays the set and actual speed values, and can switch between displaying torque/time
Equipped with safety features such as splash and overload protection

## Slide 11
Technlcal Parameter | OS20-Pro OS40-Pro |  | OS70-Pro
Maximum mixing volume[water] | 20L | 40L | 70L
speed range | 50-2200rpm | 50-2200rpm | 50~1100rpm
Speed control accuracy | 3rpm | 3rpm | ±10rpm
time range |  |  | 0-99h59min
MAXIMUM TORQUE | 40N.cm | 60N.cm | 300N.cm
Maximum viscosity | 10000mPa.s | 50000mPa.s | 100000mPa.s
Motor type | brushless dc motor | brushless dc motor | brushless dc motor
Speed display | LCD | LCD | LCD
Torque display | LCD | LCD | LCD
Overload protection display | LCD | LCD | LCD
Drill chuck clamping diameter range | 0.5~10mm | 0.5~10mm | 0.5~10mm
degrees of protoction provided byenclosure | IP21 | IP21 | IP21
data interface | RS232 | RS232 | RS232
voltage | 100-240V,50/60 Hz | 100-240V,50/60 Hz | 100-240V,50/60 Hz
Motor input and output power | 60W/50W | 120W/100W | 180W/160W
power | 70W | 130W | 200W
Size [length xwidth xheig ht] | 83×220×186mm | 83×220×186mm | 83×220x 186mm
weight | 2.8kg | 2.8kg | 3.2kg
Allow ambient temperature and humidity | 5-40℃,80%RH | 5-40℃,80%RH | 5-40℃,80%RH

## Slide 12
Centrifugal agitator Article number 18900074
Pole length 40cm
Mixing blade diameter 9cm
Paddle shaft diameter 08mm
Material:316L stainless steel
The two blades open with increasing speed,suitable for narrow mouths Round bottle,suitable for medium to high spoed use
Fan type mixing blade Article number 18900073
Pole length 40cm
Mixing blade diameter 6.8cm
Paddle shaft diameter 08mm
Material:316L stainless steel
Mid stiring performance,suitable for use at medium to low speeds
List of Mixing Paddle Series
Fan type mxing blade Zhongshi InsrumnArticle number 18900077
Pole length 35cm
Mixing blade diameter 6.8cm
Paddle shaft diameter 08mm
Material:PTFE coating
Mild stirring performance,suitable for use at medium to low speeds.
Pole length 35cm
Mixing blade diameter 6.5cm
Paddle shaft diameter 08mm
Material:PTFE coating
Standard mixing blade,suitable for medium and high speeds.
Pole length 35cm
Mixing blade diameter 8.5cm
Paddle shaft diameter 08mm
Material:PTFE coating
The two blades open with increasing Pound bottle,suitable for medium to high spoed use
Pole length 35cm
Mixing blade diameter 7cm
Paddle shaft diameter 08mm Material:PTFE coating
Suitable for mixing low viscosity media
Pole length 40cm
Mixing blade diameter 6cm
Paddle shaft diameter 08mm
Material:316L stainless steel
Suitable for mixing low viscosity media
Pole length 40cm
Mixing blade diameter 5cm
Paddle shaft diameter 08mm Material:316L stainless steel
Standard mixing blade,used at
Multiple types of agitator blades to choose from
One line agitator blade Article number 18900072
Zhongshi Instrument
Four bladed agitator blade i t Article number 18900071
nstrumen
Zhongshi
Centrifugal agitator Article number 18900078
and use at medium to high speeds.
Four baded aitator blade
Article number 18900075
speed,suitable for narrow mouths
and use at medium to high speeds.
medium to high speeds.
Article number 18900076
One line agitator blade

## Slide 13
Four blade laige mixing blade Article number 18900478
Anchor type large mxing
paddle
Pole length 60cm Mixing blade diameter Paddle shaft diameter Material:316L stainless Universal mixing blade | 10cm 08mm steel | 
Pole length 40cm
Mixing blade diameter 5cm
Paddle shaft diameter 08mm
Material:316L stainless steel
Suitable for medium to high viscosity media and medium to high speed use, Pecommendad for lin iA hommenizatinn o nrenaratinn nf tl lin ire
Fan blade larga mixing blade Pole length 60cm Mixing blade diameter 10cm Paddle shaft diameter 08mm Material:316L stainless steel | 
Universal stirring blade,suitable for samples that are prone to precipitation.
Hat blade agitator Article number 18900625
Pole length 40cm
Mixing blade diameter 6cm
Pole length 40cm
Mixing blade diameter Gcm
Paddle shaft diameter 08mm
Material:316L stainless steel
Suitable for medium to high viscosity media and low-speed use.
Pole length 60cm
Mixing blade diameter 10cm
Paddle shaft diameter 08mm
Material:316L stainless steel
With high shear force,it can be used to crush particles in mixed samples
Paddle shaft diameter 08mm
Material:316L stainless steel
Suitable for medium to low viscosity media and medium speed use.
Material:316L stainless steel
Suitable for medium tolow viscosity media,used at medium to high speeds, Reoommended for the treatment of oases in liguids
Anchor type agitator Article number 1890062
Pole length 60cm
Mixing blade diameter 10cm Paddle shaft diameter 08mm Material:316L stainless steel
Dissolved large agitator blade Article number 1890050
Runoff agitator Article number 18900626
Pole length 40cm
Mixing blade diameter 5cm Paddle shaft diameter 08mm
Spiral mixing blade
Suitable for samples sensitive to ahear forces and samples prone to delamination during atirring
Article number 1890049
Article number 1890062
Article number 18900498